## Slide 1
How to program a firmware with a programming cable
Document No. 930-00212
Rev 1.42

## Slide 2
PREPARATIONS
VCC
SWDIO
SWCLK
GND
Definition of the Pins on Solar BLE Gateway
In all of the interfaces we use, VCC is the square one

## Slide 3
PREPARATIONS
Definition of the Pins on Badge Tracker

## Slide 4
PREPARATIONS
VCC
SWDIO
SWCLK
GND
Definition of the pins on Asset Management Tracker

## Slide 5
Definition of the pins on Asset Management Tracker
PREPARATIONS
GND
SWCLK
SWDIO
VCC

## Slide 6
Definition of the pins on iBeacon
PREPARATIONS
GND
SWCLK
SWDIO
VCC

## Slide 7
The cable

## Slide 8
Definition of pins on the cable

## Slide 9
Use the connector to connect the PCB.
Then program the firmware according to the following steps beginning from page 10.
Badge Tracker PCB

## Slide 10
Connect the micro USB cable to the badge.
Then program the firmware according to the following steps beginning from page 10.
Badge Tracker

## Slide 11
Use the connector to connect the PCB .
Then program the firmware according to the following steps beginning from page 10.
Asset Management Tracker PCB

## Slide 12
STEP ONE : Download the software
1. Follow the link to download the software. https://www.nordicsemi.com/-/media/Software-and-other-downloads/Desktop-software/nRF-command-line-tools/sw/Versions-10-x-x/10-10-0-v2/nRF-Command-Line-Tools_10_10_0_Installer.exe
2. Unzip the files and get the software nRF-Command-Line-Tools_10_10_0_installer.exe.

## Slide 13
3.Install the software in three steps.

## Slide 14
3.Wait for the installation to complete, and click the finish button to exit.

## Slide 15
STEP TWO : Program the firmware
1. Make a copy of the nRF folder to Desktop.
(Please contact us to get this folder)

## Slide 17
2. Click on script recover.bat to recover readback protection.
3. Click DFU_Program.bat to program the firmware.

## Slide 18
4. The programming starts automatically. When it finishes, you should be able to hear a beeping voice from the tracker.
Press any key to continue.